Important programming

- To enter program mode: PRG    7    SAVE

- To exit program mode: SPK    SAVE

- Program 01: DAY RING

Select trunk:01-10     SAVE

Insert desired station numbers too ring.

Finish inputs to each line with SAVE

Press PRG to return to program mode

- Program 02: NIGHT RING

Select trunk:01-10     SAVE

Insert desired station numbers too ring.

Finish inputs to each line with SAVE

Press PRG to return to program mode

- Program 04: CONSOLE ASSIGNMENT

Select station group: 1-8

Input desired console extensions

Finish inputs to each line with SAVE

Press PRG to return to program mode

Note: you can only input system speed dials from a console. Night switching, when done manually, can only be done from a console.

- Program 05: system timing parameters

Page 05:

Item 05 : name feature for speed dials and extensions

Default:0                change too: 7

NOTE: this will halve the maximum number of speed dials the system is               capable of using.

- Program 05:

Page 05:

Item 01: hold recall time                        default: 1

Item 02: exclusive hold recall time        default: 1

Item 03: hold recall timeout                   default: 1

0 = 30 seconds   1= 60 seconds   9 = never

Hold recall is the time the system allows a call to remain on hold before it begins to call the station that placed the call on hold.

Exclusive hold recall is as above but only applies to calls placed on exclusive hold

Hold recall timeout this timer begins when one of the above timers has expired and a station has begun ringing. If this timer is breached the call is sent to the first console in the station group.

- Program 05:

Page 03:

Item 02:Automatic trunk search          DEFAULT: 0

0 = enabled      1 = not allowed

Item 03:Intercom call signal                 DEFAULT: 0

0 = voice          1 = ring

Automatic trunk search: this enables automatic selection of lines when you use redial or speed dials.

Intercom call signal: the call signal received by the ‘called’ phone in an intercom situation

- Program 05:

Page 04:

Item 02: dial 9 flag                               default: 1

1 = can gain access to lines by dialing nine

0 = can’t gain access to lines by dialing nine

Item 04: 12/ 24 Hour clock                  default: 0

0 = 12 hour clock               1 = 24 hour clock

- Program 05:

Page 08:

Item 08: music source selection            default: 0

Should be: 3

- Program 05:

Page 12:

Item 07: LED indication of room status

Default:0  = disabled

- = Enabled

This is for hotel sites to be able to determine a room’s status from the DSS key associated to it.

Slow flashing red:  checked out

Solid green:               room has been cleaned and is ready.

(After cleaning pick up handpiece and dial 776)

Solid red:                 station is in use

None:                            station is idle

- Program 05:

Page 13:

Item 03: caller id buffer size     default: 0 = 10 sets (24 blocks)

1 = 20 sets (12 blocks)

2 = 30 sets (8 blocks)

3 = 40 sets (6 blocks)

- Program 05:

06:

06: Automatic dropout of conference calls

Default: 3 minutes (3) options: 0,1,2,3,4,5,6,7,8,9

Note: isdn doesn’t require a timer so set too zero

- Program 05:

08:

01: hunt timer

this program modifies the time a call will ring at one

station before it searches for the next available station

default: 0 (wont search for others)

options:1-2 secs  2-4secs  3-6 secs  4-8 secs  5-15 secs

6-30 secs  7-60 secs  8-120 secs  9-254  secs

- Program 07: flexible key programming

: Select key layout you wish to modify (1-8) press save

Mic/at: changes the function of the key

Save: press save to input each key change

Dss key 1,2: these scroll through available keys to change

# Keys :00 – 19: any function

20 – 25: no function

26: for conformity please make this the directory key

(Fn: 62)

27:when programming for a system with isdn or pstn and a cli card please make this key cli history (Fn: 32)

When programming this key for a system without items as listed above please make this key Page all (Fn: 22)

28 – 29: do not touch these are the program and save keys changing these will give you headaches

- Some other useful keys to use:

Extensions: no prefix just the extension no#

Co lines:    CO: ##     01-10

Function:    Fn: ##     52 = nightswitch manually

00 = one touch speed dial

53 = call forward

54 = call forward busy

55 = call forward no answer

59 = hotel motel function (that’s all I know)

17 = check in room

18 = check out room

- Program 11: System time        press save

MM  DD  YY  HH  MM  D

EG:  02     20     02   10     40    3

NOTE: MONDAY = 1

- Program 20: daytime schedule

Item: 00 = Sunday   -   06 = Saturday       press save

Enter time: e.g.: 08 00 17 00 12 00 13 00

This will put the system into day mode at 8:00 AM

Put it on lunch between 12 & 1 PM

## And switch to night mode automatically at 5:00 PM

If lunch time is not required leave the times out

- Program 25: system reset

Item: 1 = reset minus the speed dials

Item: 2 = reset including the speed dials

Items: 3 & 4 refer to full manual

- Program 41: station settings

: Enter station number press save

Item: 1 = station group 1 – 8 assign a station to a group

Item: 2 = key group 1 – 8 assign a station to a key layout

Item: 7 = card number / port number

- Program 43: port settings

No item press mic/at to change screens then type in name

- Program 72: Indial assign

: Enter station number to assign indial too

: Enter indial number

- Program 70: isdn settings

: CD 01 – 04

: IP 01 – 03

Ensure all are set 111

- Program 83:allocate memory for cli

: Enter extension number press save

Allocate one or two blocks 01 – 24

00 = no block

E.g.: 01 02 = block 1 & 2

03 00 = block 3

00 00 = no blocks

- PROGRAM 09: SYSTEM SPEED DIALS

: ENTER SPEED DIAL CODE 100 – 599

(100 – 299 IF YOU ARE USING NAMES ON SPEED DIALS OR EXTENSIONS)

ENTER PHONE NUMBER

PRESS MIC/AT TWICE

TYPE NAME OF SPEED DIAL

### ONCE DONE PRESS SAVE

- Program 35: trunk specifications

Trunk:  xx

Item:07  ring method day

:08  ring method night

- common audible  1- linear  2-circular

3- hunt  4-  private

- program 47: hotline

station: enter station number

spd code: xxx

use this for connecting fax lines N.B. don’t actually put any speed dial into the selected speed dial entry just select the appropriate trunk you wish to use